## Slide 1
RISC-V SoC with
Virtual Memory Support
Architecture, RTL Design, UVM Verification, and Physical Design (RTL-to-GDS)
Prepared by: Noor-Ul-Ain, Nabiha Fatima Training Program: USTP Digital IC Design and Verification Project: Project 01 — RV32I-based SoC with Simplified Virtual Memory
13th September 2026
Notes: This project builds an RV32I RISC-V System-on-Chip with a simplified hardware virtual-memory subsystem: an MMU, page table, TLB, and page-fault reporting. Two areas make up most of the engineering effort and are the heart of this presentation: the UVM verification environment, and the physical design flow that carries the RTL to a manufacturable SKY130 GDS-II layout using OpenROAD. Team: Noor-Ul-Aiin and Nabiha Fatima, USTP Digital IC Design and Verification program, Project 01.

## Slide 2
INTRODUCTION
Project Overview & Motivation
2 / 13
Modern processors use virtual addressing: each program sees its own address space, translated to physical memory by a hardware Memory Management Unit (MMU).
This project implements a simplified hardware virtual-memory mechanism on an RV32I RISC-V core — an MMU with a page table, a TLB cache, and page-fault reporting.
It omits the full complexity of a multi-level SV32 walker or a complete privileged architecture, keeping the mechanism clear and demonstrable.
Goal: demonstrate, in synthesizable hardware, the same address-translation and fault-handling principles used by real processors and operating systems such as Linux.
PROGRAM VIEW
Virtual address space
(per-process)
HARDWARE MMU
Address translation
(page table + TLB)
PHYSICAL MEMORY
Instruction / Data SRAM
RISC-V SoC — Virtual Memory Support
Notes: Motivation: real processors (and OSes like Linux) give every program its own virtual address space, translated to physical memory by a hardware MMU. This project reproduces that mechanism in synthesizable hardware on an RV32I core, but deliberately simplified -- a single-level page table instead of a full multi-level SV32 walker, and no complete privileged architecture. The point isn't to build a production MMU; it's to demonstrate the same translation and fault-handling principles real hardware uses, in a design small enough to carry all the way through verification and physical layout.

## Slide 3
INTRODUCTION
Objectives & Scope
3 / 13
OBJECTIVES
Design a synthesizable RV32I core and a simplified MMU/TLB virtual-memory subsystem
Add CSR-based control (SATP, MSTATUS) and centralized exception/interrupt handling
Integrate an AXI4-Lite debug interface and UART/GPIO peripherals
Verify the design with a directed testbench and a full UVM environment
Carry the design through a complete RTL-to-GDS physical design flow, plus a parallel FPGA build
SCOPE
INCLUDED
Single-level page table (1024 entries)
4 KB page size
Hardware translation, TLB caching, and page-fault handling
OUT OF SCOPE
Two-level SV32 page-table walk
Full privileged modes (M / S / U)
Interrupt controller and operating system
RISC-V SoC — Virtual Memory Support
Notes: Objectives to mention out loud: (1) synthesizable RV32I core + simplified MMU/TLB, (2) CSR-based control via SATP/MSTATUS plus centralized exception handling, (3) AXI4-Lite debug interface and UART/GPIO peripherals, (4) two-pronged verification -- directed testbench and full UVM, (5) a complete RTL-to-GDS physical design flow plus a parallel FPGA build. On scope: the project keeps a single-level, 1024-entry page table and 4KB pages rather than the two-level SV32 walk, and does not implement full M/S/U privileged modes, an interrupt controller, or an OS -- this keeps the translation/TLB/fault mechanisms clear and demonstrable while still being small enough to reach a real physical layout.

## Slide 4
SYSTEM ARCHITECTURE
Top-Level Architecture
4 / 13
RISC-V SoC — TOP LEVEL
RV32I CORE
FSM: Fetch → Execute →
Memory → Writeback
MMU + TLB
Address translation
+ page-fault check
PERIPHERALS
AXI4-Lite • UART • GPIO
INSTR / DATA SRAM
Physical-address access
(Harvard-style)
CSR UNIT
SATP • MSTATUS
EXCEPTION HANDLER
Faults + interrupts →
trap vector
RV32I core issues virtual addresses for instruction fetch and data access
MMU (backed by TLB) resolves virtual → physical addresses before memory access
CSR unit holds translation/status state; exception handler arbitrates faults and interrupts
Top level exposes an AXI4-Lite debug port plus UART/GPIO pins
RISC-V SoC — Virtual Memory Support
Notes: Walk through the data flow: the RV32I core issues virtual addresses for both instruction fetch and data access. The MMU, backed by a TLB, resolves these to physical addresses before they reach instruction/data memory. The CSR unit holds translation and status state (SATP, MSTATUS); the exception handler arbitrates faults and interrupts. The top level also exposes an AXI4-Lite debug port and UART/GPIO pins. Key parameters to have ready if asked: 32-bit ISA with 32 registers (x0-x31); 4KB page size; 16-entry fully-associative TLB; 1024-entry single-level page table; 100 MHz target frequency; SkyWater SKY130 (130nm) as the target ASIC process; Digilent Arty A7-100T as the target FPGA.

## Slide 5
PROCESSOR CORE
RV32I Core
5 / 13
Multicycle, FSM-based RV32I implementation with a 32-entry register file
FETCH: issues PC to the MMU as a virtual address
EXECUTE: decodes and runs the ALU operation
MEMORY: issues load/store addresses to the MMU
WRITEBACK: commits the result to the register file
Every fetch and load/store is issued as a virtual address to the MMU — never directly to memory
FETCH
EXECUTE
MEMORY
WRITEBACK
register file commit → next fetch cycle
CORE ↔ MMU HANDSHAKE
Every fetch and load/store address crosses to the MMU via a valid/ready handshake, with a page-fault return path — the architectural boundary that enables the virtual-memory subsystem.
Category | Instructions
Arithmetic (reg/imm) | ADD, SUB, AND, OR, XOR, SLT, SLTU, ADDI, ANDI, ORI, SLLI, SRLI, SRAI
Loads / Stores | LB, LH, LW, LBU, LHU / SB, SH, SW
Control transfer | JAL, JALR, BEQ, BNE, BLT, BGE, BLTU, BGEU
Upper imm. / System | LUI, AUIPC / ECALL, EBREAK, CSRRW, CSRRS, CSRRC
RISC-V SoC — Virtual Memory Support
Notes: The core is a multicycle, FSM-based RV32I implementation with a 32-entry register file, cycling through FETCH (issue PC to the MMU as a virtual address), EXECUTE (decode and run the ALU op), MEMORY (issue load/store addresses to the MMU), and WRITEBACK (commit to the register file). The key architectural point: every single fetch and load/store goes through the MMU as a virtual address -- never straight to memory. That core-to-MMU handshake (valid/ready plus a page-fault return path) is what makes the rest of the virtual-memory subsystem possible. The instruction set covers standard RV32I: arithmetic/immediate ops, loads/stores, control transfer (branches/jumps), and upper-immediate/system instructions including the CSR instructions and ECALL/EBREAK.

## Slide 6
VIRTUAL MEMORY
Virtual Memory Subsystem: MMU & TLB
6 / 13
A virtual address is split into a Virtual Page Number (VPN) and a page offset
The MMU indexes a single-level, 1024-entry page table with the VPN to find a Physical Page Number (PPN) and permission flags
A 16-entry fully-associative TLB (a CAM comparing all entries in parallel) caches recent translations
Most accesses complete in one cycle instead of paying for a full page-table lookup
The TLB is flushed whenever SATP changes — a new address space invalidates all cached translations
VIRTUAL ADDRESS
VPN + Page Offset
16-ENTRY TLB (CAM)
Parallel compare of cached translations
TLB HIT
PPN returned
(1 cycle)
TLB MISS
Page-table walk
(1024-entry)
PTE Field | Meaning
V / R / W / X | Valid / Read / Write / Execute permission
U / G | User-accessible / Global (not flushed on address-space switch)
A / D | Accessed / Dirty
PPN | Physical page number this entry maps to
RISC-V SoC — Virtual Memory Support
Notes: A virtual address splits into a Virtual Page Number (VPN) and a page offset. The MMU indexes a single-level, 1024-entry page table with the VPN to find a Physical Page Number (PPN) plus permission flags. A 16-entry fully-associative TLB -- a CAM that compares all entries in parallel -- caches recent translations so most accesses complete in one cycle instead of paying for a full page-table lookup. Page table entries carry V/R/W/X (valid/read/write/execute), U/G (user-accessible/global), A/D (accessed/dirty), and the PPN itself. Worth noting if asked: G (global) entries are not flushed on an address-space switch, unlike ordinary entries.

## Slide 7
VIRTUAL MEMORY
Address Translation Flow
7 / 13
1
Core issues VA
for a fetch or data access
2
MMU checks TLB
compares all entries (CAM)
3
Hit → PA returned
immediately, same cycle
4
Miss → page-table walk
check valid bit + permissions
5
Install in TLB
valid & permitted access
PAGE FAULT PATH
An invalid or permission-violating access raises a page fault instead of completing the translation
Page faults are merged with core exceptions and external interrupts by the exception handler into a single trap decision
CONCURRENT & CONSISTENT
Separate translation state machines handle the instruction and data paths independently — a fetch and a load/store can translate at the same time
The TLB is flushed whenever SATP changes, since a new address space invalidates every previously cached translation
RISC-V SoC — Virtual Memory Support
Notes: Step through the translation flow: the core issues a virtual address to the MMU for a fetch or data access. The MMU checks the TLB first -- on a hit, the physical address returns immediately, same cycle. On a miss, the MMU walks the page table and checks the PTE's valid bit and permissions; a valid, permitted access computes the physical address and installs it in the TLB, while an invalid or permission-violating access raises a page fault instead. Two details worth calling out: separate translation state machines handle the instruction and data paths independently, so a fetch and a load/store can be translating at the same time; and the TLB is flushed whenever SATP changes, since a new address space invalidates every previously cached translation.

## Slide 8
INTEGRATION
SoC Integration & Interfaces
8 / 13
CSR unit holds SATP (MMU translation base, flushes TLB on write), MSTATUS, and a cycle counter — accessed via CSRRW / CSRRS / CSRRC
Exception handler merges core exceptions (illegal instruction, ECALL/EBREAK), MMU page faults, and external interrupts into one trap decision using MSTATUS / MIE / MIP and MTVEC
An AXI4-Lite subordinate port (plus an AXI4 arbiter for multi-master use) exposes on-chip registers to an external host/debugger
UART and GPIO pins support board-level demonstration
Instruction and data memory are separate 4096-word single-port SRAMs (Harvard-style), accessed only with the physical address the MMU produces
RV32I CORE + MMU/TLB
CSR UNIT
SATP • MSTATUS • cycle cnt
EXCEPTION HANDLER
MIE / MIP / MTVEC
AXI4-LITE SUBORDINATE + ARBITER
Debug/host register access
UART
Board-level demo
GPIO
Board-level demo
RISC-V SoC — Virtual Memory Support
Notes: Integration summary: the CSR unit holds SATP (the MMU's translation base register, which flushes the TLB whenever it's written), MSTATUS, and a cycle counter, all accessed via CSRRW/CSRRS/CSRRC. The exception handler merges core exceptions (illegal instruction, ECALL/EBREAK), MMU page faults, and external interrupts into a single trap decision -- cause, interrupt vs. exception, and target handler address -- using MSTATUS/MIE/MIP and MTVEC. On the bus side, an AXI4-Lite subordinate port (plus an AXI4 arbiter for multi-master use) exposes on-chip registers to an external host or debugger, while UART and GPIO pins support board-level demonstration. Instruction and data memory are kept as separate 4096-word single-port SRAMs in a Harvard-style split, and both are only ever accessed with the physical address the MMU produces -- never a virtual one.

## Slide 9
IMPLEMENTATION
Implementation & Tools
9 / 13
Stage | Tool(s) | Role
RTL Design | SystemVerilog | Core, MMU/TLB, CSR, exception handler, SRAM, AXI arbiter, top-level SoC
Directed Simulation | tb_riscv_soc.sv | Fast self-checking bring-up: reset, PC advance, GPIO, UART loopback
UVM Verification | SystemVerilog UVM | 4-agent environment with scoreboards, coverage, and 7 sequences
Synthesis | Yosys 0.62 | Maps RTL to SKY130 standard cells
Floorplan / Place / Route | OpenROAD (nPlace, TritonCTS, Router) | Floorplanning, placement, clock-tree synthesis, routing
GDS Generation | Magic + KLayout | Streams the final riscv_soc_top.gds layout
Sign-off | Magic, KLayout (DRC) • Netgen (LVS) | Design-rule and layout-vs-schematic verification
FPGA Build | Makefile / flow.json / XDC | Targets Digilent Arty A7-100T for functional demo
Physical design follows the open-source OpenLane/OpenROAD flow targeting the SkyWater SKY130 (130 nm) process (sky130A PDK)
RISC-V SoC — Virtual Memory Support
Notes: Tool rationale, in case you're asked why each was chosen: Yosys 0.62 performs synthesis, mapping the RTL to SKY130 standard cells. OpenROAD handles floorplanning, placement (nPlace), clock-tree synthesis (TritonCTS), and routing. Magic and KLayout generate and cross-check the final GDS-II layout, and Netgen performs LVS (layout-vs-schematic). The whole physical design flow follows the open-source OpenLane/OpenROAD flow targeting the SkyWater SKY130 (130nm) process, specifically the sky130A PDK. In parallel, a Makefile/flow.json-based FPGA build targets the Digilent Arty A7-100T, using an XDC constraints file and an RTL wrapper for board I/O -- meant to demonstrate address-translation behavior via UART and GPIO/LEDs on real hardware.

## Slide 10
VERIFICATION & RESULTS
Verification, Simulation & Sign-off Results
10 / 13
UVM ENVIRONMENT
One top-level env with 4 independent agents — GPIO, UART, AXI4-Lite, interrupt — each with a sequencer, driver, and monitor
Each agent has a dedicated scoreboard; a top-level scoreboard aggregates results into one pass/fail verdict per test
Functional coverage tracks GPIO patterns, UART bytes, AXI address ranges, and interrupt timings
7 reusable sequences (gpio_passthrough, uart_echo, axi_write/read, interrupt, reset, regression)
Sign-off Check | Result
DRC (Magic + KLayout) | 0 errors, 0 warnings
LVS (Netgen) | 100% match — 363/363 cells, no floating nets
STA (Typical/Slow/Fast) | Positive setup & hold slack on every corner
Power (est. @ 100 MHz) | ~3.5 mW total, IR drop < 45 mV
Figure: Full-chip layout in OpenROAD — routing-congestion heat map, met1–met5 stack, I/O ring, and power straps.
RISC-V SoC — Virtual Memory Support
Notes: UVM detail worth having ready: one top-level environment contains four independent agents -- gpio_agent, uart_agent, axi_agent, interrupt_agent -- each with its own sequencer (arbitrates stimulus), driver (converts transactions to pin-level activity), and monitor (passively observes and reconstructs transactions; never drives a signal). Each agent has its own scoreboard, and a top-level scoreboard aggregates all of them into one pass/fail verdict per test. Functional coverage groups record which GPIO patterns, UART bytes, AXI address ranges, and interrupt timings have actually been exercised. Seven reusable sequences drive the agents: gpio_passthrough_seq, uart_echo_seq, axi_write_seq, axi_read_seq, interrupt_seq, reset_seq, and regression_seq (which runs all the others back-to-back as a full smoke/regression pass). Physical design numbers, stage by stage, if you want more depth than the slide shows: Synthesis (Yosys) mapped the RTL to 126 SKY130 cells (4 flip-flops, ~114 combinational, 8 buffers), ~450 um^2, ~2.5mW estimate. Floorplanning produced a 3600x3600um die / 3500x3500um core (12.96 mm^2) at 75% target utilization. Placement (OpenROAD nPlace) placed 363 cells with HPWL of 5,376um and average displacement of 1.0um. Clock tree synthesis (TritonCTS) served 44 flip-flop sinks via 6 buffers in 2 levels, achieving 0.18ns clock skew against a <0.5ns spec. Routing used 4 metal layers (M1-M4), ~500 nets, 79,425um total wire, 100% routed with 0 DRC violations. GDS generation (Magic + KLayout) produced riscv_soc_top.gds (591KB), 363 instances, ~6,880 shapes. Sign-off: DRC clean (0 errors/warnings across metal, via, density, antenna rules), LVS 100% match (363/363 cells, no floating nets), and STA closed with positive slack on every corner (setup +0.4/+0.2/+0.6ns; hold +0.15/+0.10/+0.20ns for typical/slow/fast). Overall, 72 of 80 flow stages completed -- a clean-sign-off, tapeout-ready GDS-II layout.

## Slide 11
DESIGN CONSIDERATIONS
Challenges & Design Considerations
11 / 13
Scoped Virtual Memory Model
A single-level page table (vs. two-level SV32) and no full privileged modes/interrupt controller/OS keep the translation, TLB caching, and fault-handling mechanisms clear and demonstrable, while still reaching a physical layout.
TLB Coherency on Context Switch
The TLB must be flushed on every SATP write, since a new address space would otherwise leave stale, incorrect translations cached.
Concurrent Translation Paths
Instruction and data accesses use separate translation state machines so a fetch and a load/store can be in translation at the same time without interfering.
Clock-Tree Timing Margin
TritonCTS achieved 0.18 ns clock skew across 44 flip-flop sinks, well within the < 0.5 ns specification.
Flow Completion Status
72 of 80 physical-design flow stages completed; the design reached clean sign-off (DRC/LVS/STA) and a GDS, with remaining stages tracked as follow-on work.
RISC-V SoC — Virtual Memory Support
Notes: These are the main technical talking points if challenged in Q&A: (1) the scope trade-off -- a single-level page table instead of two-level SV32, and no full privileged modes/interrupt controller/OS -- was a deliberate choice to keep the translation/TLB/fault mechanism clear and demonstrable while still reaching a real physical layout; (2) TLB coherency requires a full flush on every SATP write, since otherwise a new address space would incorrectly reuse stale cached translations; (3) instruction and data paths use independent translation state machines so they don't block each other; (4) the clock tree closed with 0.18ns skew against a <0.5ns spec, showing solid timing margin; (5) 72 of 80 flow stages were completed -- worth being upfront that this is a clean sign-off and tapeout-ready GDS, but not literally every flow stage, and framing the remainder as tracked follow-on work rather than glossing over it.

## Slide 12
CLOSING
Conclusion
12 / 13
ACHIEVED
A virtual-memory-capable RISC-V SoC: RV32I core, MMU/TLB, CSR-based control, and exception handling
Verified through a four-agent UVM environment with dedicated scoreboards, coverage, and seven test sequences
Carried through a complete physical design flow to a clean-sign-off, tapeout-ready SKY130 GDS-II layout
A parallel FPGA build path targeting the Digilent Arty A7-100T
Together these demonstrate the full lifecycle from RTL through verification to physical layout.
RISC-V SoC — Virtual Memory Support
Notes: Closing summary to read almost verbatim if needed: this project implements a virtual-memory-capable RISC-V SoC -- RV32I core, MMU/TLB, CSR-based control, and exception handling -- verified through a four-agent UVM environment with dedicated scoreboards, coverage, and seven test sequences, and carried through a complete physical design flow to a clean-sign-off, tapeout-ready SKY130 GDS-II layout, alongside a parallel FPGA path. Together these demonstrate the full lifecycle from RTL through verification to physical layout. Natural next steps if asked what's left: pre-load the MMU's page table so translations can be exercised end-to-end, replace the current UART/GPIO pass-through stubs with real controllers, and add a UVM agent that targets the core-MMU-TLB datapath directly (TLB hit/miss, page-table walks, page faults).

## Slide 13
Thank You
Questions & Discussion
RISC-V SoC with Virtual Memory Support — RTL to GDS-II
Notes: If asked a question you're unsure of, it's fine to say a detail is out of scope for this simplified model (e.g., no multi-level page walk, no full privileged modes) -- that's a documented, deliberate design boundary, not an oversight.